| CONsTRUCTION OF PrIMARY BLOCK PATTERNS – FITTED BODICE BLOCK SIZE 38 Literature: Rundschau: Sammelband Schnittkonstruktionen fűr Damenbekleidung nach Műller & Sohn, Műnchen 1997 |
| --- |
| Measurements required to draft the block Body measurements: (h)–Height, (bg)–Bust girth, (nwl)–Nape to waist (back length), (wg)–Waist girth, (hg)–Hip girth, (wfl)–Front length to waist, (bfl)–Front length to bust Garment measurements:(sll)–Sleeve length, (bll)–Garment length (Blouse length) Primary block patterns corresponds to size 38 of chart DOB Main Measurements: h = 168 cm, bg = 92 cm, wg = 70 cm, hg = 98 cm, sll = 60 cm Auxiliary Measurements for size 38: ad armhole depth 1/10 bg + 10.5 = 19.7 cm nwl Nape to waist (back length) 1/4 h – 1 = 41 cm Crutch depth = Garment length ad + nwl = 60.7 cm nw width of neckline 1/10 of 1/2 bg + 2 = 6.6 cm bfl Front length to bust 1/4 bg + 3 až 5 = 27 cm (see table) Fr neck point to bust point (calculated or measured) wfl Front length to waist nwl + 4.5 = 45.5 cm (see table) Fr neck point to waist point (calculated or measured) bw Across back (back width) 1/2 bw = 1/8 bg + 5.5 = 17 cm aw Width of armhole 1/8 bg – 1.5 = 10 cm fw Across front (front width) 1/4 bg – 4 = 19 cm sh shoulder sh = 12.4 cm (see table) |
| Step | Measurement | Designation | Formula | Calculation |
| Back and Front Pieces |
| 1. | Back centre line and neck line | 1 n |  |  |
| 2. | Armhole depth | N1B1 | ad + (2 to3) | 21.7 cm |
| 3. | Nape to waist (back length) | N1W1 | nwl | 41.0 cm |
| 4. | Crutch depth | N1H1 | nwl + ad | 60.7 cm |
| 5. | Crutch depth = Garment length | N1L1 = N1H1 | bll | 60.7 cm |
| 6. | Horizontal plains | b, w, h 1 |  |  |
| 7. | Formation of BC | H1H11 | k = 2 | 2.0 cm |
| 8. | Diversion of back centre line | N1H11 B11, W11 |  |  |
| 9. | Across back (back width) | B11B3 | bw + (1,5 to 2) | 18.5 cm |
| 10. | Width of armhole – back bodice | B3B4 | 2/3 (aw + (2.5 to 3.5)( | 8.7 cm |
| 11. | Free place | B4B4´ | k | 5.0 cm |
| 12. | Width of armhole – front bodice | B4´B5 | 1/3 [aw +(2.5 to 3,5)] | 4.3 cm |
| 13. | Across front (front width) | B5B7 | fw + (1.5 to 2) | 20.5 cm |
| 14. | Controled bust width | B11B4 + B4´B7 | 1/2 bg + (5.5 to 7.5) | 51.5 to 53.5 cm |
| 15. | Construction bust point | B7B6 | 1/10 bg + 1 | 10.2 cm |
| 16. | Vertical plains | 3, 4, 4´, 5, 6, 7 b |  |  |
| 17. | Width of neckline | N1N2 | nw | 6.6cm |
| 18. | Back neck rise | N2N4 n | k = 2 | 2.0 cm |
| 19. | Shoulder line slope | N3Sh3 | k = 1 to 1.5 | 1.5 cm |
| 20. | Shoulder | N4Sh3 N4Sh4 | sh + 1 + 0.5 | 13.9cm |
| 21. | Balance mark | B3B31 | 1/4 [ad (constr.) –1 to 1.5] | 5.05cm |
| 22. | Balance mark (finish) of sleeve - BB | B31B32 | k = 1.3 | 1.3 cm |
| 23. | Transferred measurement from BB to FB | B5B51 | B3B31=B5B51 |  |
| 24. | Balance mark of sleeves-FB | B5B52 | 1/4 aw ( constr.) | 3.3 cm |
| 25. | Sloupe of schoulder FB | B5Sh5 | B3Sh3 – 1 to 1,5 |  |
| 26. | Part of radius | r1 | r1 (B5;r = B5Sh5) |  |
| 27. | End of shoulder line | Sh5Sh4´ | 1/20 bg - 1 to 2 | 3.6cm |
| 28. | Front length to waist | W6N6 | wfl | 45.5 cm |
| 29. | Front length to bust | N6B61 | bfl | 27.0 cm |
| 30. | Part of radius | r2 | r2(B61; r=B61N6) |  |
| 31. | Point of shoulder to neck ( schoulder FB | N61 r2 r3 ( Sh4´N61 | r3 (Sh4´; r =N4Sh4 –0.5 ) |  |
| 32. | Help line | Sh4´B51 |  |  |
| 33. | Neck line of FB | N61 7 n N7 n 7 |  |  |
| 34. | Width of neckline | N7N61´ | nw | 6.6 cm |
| 35. | Neckline depth | N7N71 | nw + (1 to 1.5) | 8.1 cm |
| 36. | Help line to draft neck | N7B5 |  |  |
| 37. | Point to draft neck | N7N8 | nw + (0.5 ) | 7.1 cm |
| 38. | Location of bust dart | N61Sh6 | N61´N6 |  |
| 39. | Bust dart | Sh6B61=B61Sh6´ | N61´Sh6´ |  |
| 40. | Check hip measurement | H7Hx | 1/2 hg + (3 to 5) | 49.0 cm + 3 to 5 |
| 41. | Widening on hip line | H4H41 = H4´H41´ | 1/2 H11Hx |  |
| 42. | Check waist measurement | W5W71 | 1/4 wg | 17.5 cm |
| 43. | Setting waist dart | W71Wx | 1/2 wg + (5 to 10) | 35.0 cm + 5 to 10 |
| 44. | Waist dart – side seam | W4W41 = W4´W41´ | k = 1 | 1.0 cm |
| 45. | Waist line increase | W41W42 = W41´W42´ | k = 1 | 1.0 cm |
| 46. | Location of waiste dart of BB | W11W2 | 1/3 bw + 2 | 8.2 cm |
| 47. | Width of waist dart of BB | W2W21 = W2 W21´ | 1/2 (W11Wx – 2) 2= ( 2x 1 ) |  |
| 48. | Length of waist dart of BB | W2H2 = W2B2 | k = 14 to 16 | 15.0cm |
| 49. | Central line of waist dart | H2B2 ║ H11N1 |  |  |
| 50. | Width of waist dart of FB | W6W61 = W6W61´ | 1/2 W71W7 |  |
| 51. | Length of waist dart of FB | W6H6 = W6B62 | k = 14 až 16 | 15.0cm |
| 52. | Shoulder-blade line | B3Shb3 shb | 1/2 ad - (1 to 1.5) |  |
| 53. | Widening of back width | Shb3Shb31 | k = 1 | 1.0 cm |
| 54. | Width of back Shoulder-blade dart | Sh b31 Shb 32 = Shb 31 Shb 32´ | k = 0.5 to 1 | 0.5 cm |
| 55. | Position of Shoulder-blade dart | N4Sh2 ( 2´ | k = 3 to 5 |  |

| PRIMARY BLOCK PATTERN – semi fit sleeve |
| --- |
| Construction measurements: sll Sleeve length = 60.0 cm wrw Wrist width = (28 cm Construction measurements ( from BB and FB): AdFB armhole depth (F,B) = (39.5 cm ag armhole Girth = (46.9 cm aw armhole width = (13.3 cm ah Armhole heigth (depth of sleev head) = ½ AdFB - (1/10 aw+ 1 to 2) = (17.0 cm |
| P.č. | Rozměr | Konstrukční úsečka | Vzorec | Kontrol výpočet |
|  | Forarm line and shoulder line | 5 sh |  |  |
|  | Armhole heigth | Sh5B5 | ah | 17.0 cm |
|  | Sleeve length | Sh5Wr5 | sll | 60.0 cm |
|  | Bust and wrist lines | b, wr 5 |  |  |
|  | Increase of wrist line | Wr5 Wr 51 | k = 2 cm | 2.0 cm |
|  | Elbow line | B5E5 e | 1/2 B5Wr51 –1 |  |
|  | Balance mark FB and sleeve | B5B52 | 1/4 aw | 3.3 cm |
|  | Back arm line | B52Sh3 = r1 3 | r1(B52; r = 1/2 ag – (0,5 to 1)) | 23.0cm |
|  | Auxiliary points of head sleeve | Sh5 Sh 4 Sh 4 | 1/2 Sh 5 Sh 3 +1 |  |
|  | ,, | Sh 4 Sh 41 | 1/2 Sh 4 Sh 5 |  |
|  | ,, | B 52 Sh 51 | 1/2 B 52 Sh 41 |  |
|  | ,, | Sh 3 Sh 31 Sh 31 | 1/4 aw – 0.5 | 2.8 cm |
|  |  | B3B4 | ½ B3B5 + 1 |  |
|  | Auxiliary line | Sh 31 Sh 4 |  |  |
|  | Auxiliary point | Sh 31 Sh 32 | k = 0.5 cm | 0.5 cm |
|  | Increase bust line | b´ ║ b | k = 0.5 | 0.5 cm |
|  | Narrowing in elbow | E3 E31 | k = 1 | 1.0 cm |
|  | Narrowing in elbow | E5 E51 | k = 1 | 1.0 cm |
|  | Narrowing in low side | Wr51Wr52 | k = 1 | 1.0 cm |
|  | Sleeve width | Wr52Wr3 | 1/2 wrw | 14.0cm |
|  | Rendering head (crown) of sleeve | B52 Sh51 Sh4 Sh31 B52 |  |  |
|  | Rendering dormant of sleeve | B52 E51 L52 L3 E31 Sh31Sh4 B52 |  |  |
|  | Arc distance transferred from the FB to the sleeve line to determine the distribution of sleeve | B52 C | B52B4´ from the FB |  |
|  | Line cutting sleeve | c´ ║ 5´ |  |  |
|  | Balance mark (BB-Sleeve) | C = C´ C´ B32 | B4B32 from the BB + (0.5 to1) |  |
|  | Opening sleeve (see picture) | in front according the forearm line (5´) in the back according the back arm line (3´) (see picture) |